## Slide 1: Hotspotters Geothermal Presentation
James Hiu, Data Consultant
Tony Peng, Development Engineer
Payam Akto, Geothermal Geologist
Crystal Zhao, Associate Machine Learning Developer

## Slide 2: Overview
5
Summarize the work
Describe areas for future work and consideration
4
Insights and Discoveries
Summarize our key insights and recommendations
3
Other considerations
discuss the business, social, technology and environment needs
Technical Requirements
Summarize the data procedures and areas for objective assessment
2
1
Case Statement
Introduce the scenario and our approach

## Slide 3: Thermal Energy from retrofitting oil wells - What makes a well viable?
Science
(Temperature)
Business
Environmental
Social
Technical Requirements:
Will the site provide enough energy?
How can we accurately assess the temperature of the oil well?
Business development needs:
What are some of the operational and technology decisions?
Social impacts:
How many people will the produced energy serve?
Environmental impacts:
What are the effects to the natural environment and wildlife?
Case Statement-Problem?
Regulation

## Slide 4: Practical Needs - Will the well provide Energy?
Lindal's diagram of geothermal energy usage denotes that
  60oC+ would be viable for binary power
  140oC+ would be viable for conventional power
We are provided temperature information for each well (BHT), but the analysis is not that simple
Notes: EDA is the process of looking

## Slide 5: Practical Needs - How to accurately determine a well’s temperature?
A
Exploratory Data Analysis
B
D
Generating Model and Explainability
Iteration
C
Modeling Process
Feature Engineering Process
•We used an iterative process, project pipeline, build an accurate and predictive model.

## Slide 6: Perform Exploratory Data Analysis
Eaglebine TrueTemp vs BHT
Duvernay TrueTemp vs BHT
Pearson Correlation=0.75
Pearson Correlation=0.84
Measured Temperature
Subsea - Depth
Latitude
Longitude
Test Type
TSC or ORT
Eaglebine
Duvernay
Examine the information we were provided for strong correlations
Four promising features were found, common to both basins
Important features specific to individual basins were also discovered
Notes: TSC or ORT -time since circulation or original recorded time
Test Type - DST, LRT, CRS

## Slide 7: Feature Engineering and Outlier Reduction
Outlier treatment enhanced model accuracy
Grouped wells into 500 meter sub-sea-level depth ranges and looked for wells in ranges that were too cold or too hot with comparable wells

## Slide 8: Modeling PerformanceSummary
The best performing model scored 3.65 MAE
Applying Gradient Boosting Regressor to the Duvernay and Eaglebine dataset separately

## Slide 9: Comparing Geothermal Potential Between Basins
Duvernay Play, Alberta, Canada
Eaglebine Play, Texas, US
Type of System: low-temperature, sedimentary
Av. Thermal Gradient : 31.6 oC/km
Av. Temperature: 61.1 oC @2km
Av. Formation Gross Thickness: 380m (Beaverhill lk., Elk pnt. G.)
Av. Elevation: 1,020 m (Wabamun G.)
Volumetric Modeling (stored heat): 56.7 MWe
Type of System: low-temperature, sedimentary, geopressured
Av. Thermal Gradient: 35.5 oC/km
Av. Temperature: 95 oC @2.7km
Av. Formation Gross Thickness: 538m (Woodbine F.)
Av. Elevation: 2,223 m (Buda and underlaid)
Volumetric Modeling (stored heat): 151.3 MWe

## Slide 10: Operational Needs: Retrofitting Technology Considerations 1- Heat extraction - open loop performs better than closed loop 2- Lower Temperature wells, consider drilling deeper or using a lower boiling point liquid. 3- Closed loop, business benefit of no additional drilling Open-loop vs Closed-loop

## Slide 11: Business Needs: Which are the best Candidate Wells?
Eaglebine Play, Texas, US
Prospect Area: E Edson, Fox Creek
Prospect Area: S-SE San Antonio, E-NE Austin
Duvernay Play, Alberta, Canada

## Slide 12: Socio-Economic Impacts Alberta, CAN vs. Texas, US Accessibility to market and energy demand (end-user needs) Population: 4.3 million, 2019 Advocative regulation and policy no regulatory framework exist R&D Programs no significant R&D program (early stage) Successful projects no power generation (some projects at early stages- Alberta #1, DEEP, EAVER) Power grid and infrastructure ~ 26,000 km of transmission lines and 235 generating stations. Accessibility to market and energy demand (end-user needs) Population: 29 million, 2019 Advocative regulation and policy more mature regulatory framework in petroleum industry (ready to pivot quicker) R&D Programs Several R&D funds by Department of Energy Successful projects Several binary plants are generating power from low-temperature resource Power grid and infrastructure ~75,000 km of transmission lines and more than 550 generation units.

## Slide 13: Environmental Impacts
Geothermal is a Green source of energy!
The energy source is available 24/7 compared to other green sources such as wind and solar
Near zero greenhouse gas emissions (50g of CO2 over a 30-year project lifespan)

## Slide 14: Data Wish List
Business Considerations
The cost of retrofitting an oil well into a geothermal energy plant The cost of operating the geothermal energy plant The estimated revenue that could be generated producing this type of energy Potential cost sharing from oil company that would be in charge of decommissioning the well. Potential for political funding/tax benefits due to green energy / job creation initiatives
Social Impacts
The estimated number of jobs created at the plant The estimated number of jobs displaced by the creation of the plant The cost savings to potential customers consuming this type of energy
Environmental Impacts
The estimated cost savings from environmental damage1 Noise level and proximity to local population. Ground temperature change and and impacts to plant and wildlife. Compared to a conventional geothermal well development project, savings in terms of: - deforestation (sq. miles) - disposal of waste liquid

## Slide 15: References
King GE, Valencia RL. Environmental Risk and Well Integrity of Plugged and Abandoned Wells. Paper presented at SPE Annual Technical Conference and Exhibition, 27-29 October, Amsterdam, The Netherlands Society of Petroleum Engineers;2014. https://doi.org/10.2118/170949-MS
Jundika CK, Muhammad SS, Zulfan AP,Juliana Z, Wahyu C, Agus PS. Geothermal energy extraction using abandoned oil and gas wells: Techno-economic and policy review
Axelsson, G., 2016. Nature and Assessment of Geothermal Resources, Presented at SustainableDevelopment Goal (SDG) Short Course I, UNU-GTP & LaGeo, Santa Tecla, El Salvador,September 4-10.
Davis, M. G., D. S. Chapman, T. M. Van Wagoner, and P. A. Armstrong, 2007. Thermalconductivity anisotropy of metasedimentary and igneous rocks, J. Geophysical Res., 112,B05216, doi:10.1029/2006JB004755.
Hickson, C.J. 2015. Resource Management Plan: Reservoir Monitoring, Internal Report for HS Orka(Tuya Terra Geo Corp. October 15, 2015), 57 pages.
Hickson, C.J., and Yehia, R., 2014. The Geothermal Exploration and Development Process:Graphical Representation Path to Optimal Decision Making, Geothermal Resources Council,Transactions, Volume 38, 2014 www.geothermal.org
Peters K. E. and Nelson, P.H., 2009. Criteria to Determine Borehole Formation Temperatures forCalibration of Basin and Petroleum System Models, Search and Discovery, Article #40463,5-15http://www.searchanddiscovery.com/pdfz/documents/2009/40463peters/ndx_peters.pdf.html
Williams, C. F., 2007. Updated Methods For Estimating Recovery Factors For GeothermalResources. Proceedings, Thirty-Second Workshop on Geothermal Reservoir Engineering.Stanford University, January 22–24, 2007, SGP-TR-183, 7 pages.